MOVING DECK

Manual Over-ride Procedure

(electric flag/lock system)

8,000-10,000Kg

# DECK MANUAL OVERRIDE – SERVICE ENGINEERS ONLY

Important Power Pack Control Valve Settings:

- The valve on the power pack must be in the correct positions for the deck to operate. The valve is shown in the picture showing the Power Pack

- The LIFT/LOWER VALVE has a red button which should be ‘in’.

To manually lower the deck:

- Ensure the travelling locks are retracted clear of the deck. This can be done by operating them electrically from the manual switches in the Sanube box, or if no power, they can be forced back by strong hand pressure.

- Pull out the red button on the top of the solenoid valve and hold out against the spring. Ensure cap is pulled fully out to over ride the valve.

- With your assistant observing the rear of the trailer, ensure there is no operator under the deck and ensure there are no obstructions under the deck.

- Pull the black T- handle on the outside of the powerpack to operate the lifting cylinder safety valve and the deck will descend. This valve must be pulled and held to allow the deck to move. The valve itself can be found between the chassis main rails towards the wheels, on the foot of the main hydraulic cylinder.

- Ensure all valves are returned to normal operation after use.

To Manually Raise the Deck:

- Ensure the lifting valve and safety valve are in the operating positions. (not pulled out)

- Operate the hand pump to lift the deck.

- This will be a very slow operation, and may only be needed if the deck is resting on the travelling locks and preventing them from being retracted.